## Slide 1: Spoiler Alert!
April 30, 2019
Julio Soto, Mien Nguyen, Kushal Kusram, Jeremy Henry
CSCI 5593 – Advanced Computer Architecture
Department of Computer Science & Engineering

## Slide 2: Agenda
Recap
Implementation Plan
Implementation
Results
Mitigation
Future Work
Out of Scope Work
Questions

## Slide 3: Recap

## Slide 4: Recap
Vulnerability in Intel Core Processors which exploits Intel's Memory Order Buffer
OS independent
Works from virtual machines and sandboxed environments

## Slide 5: Recap
CPUs
  Affected
    Intel - proprietary memory disambiguation and dependency resolution logic
  Not affected
    ARM
    AMD
      “...We believe that our products are not susceptible to this issue because AMD processors do not use partial address matches above address bit 11 when resolving load conflicts.”

## Slide 6: Recap
Intel uses a proprietary memory disambiguation and dependency resolution logic to predict and resolve false dependencies
Dependency resolution logic suffers from an unknown false dependency
Exploited to leak information about physical page mappings.

## Slide 7: Recap
Why is this important?
  Microarchitectural attacks utilize this leakage of page mappings
  Enhances speedup of existing attacks significantly
  Possibility of new attacks

## Slide 8: The Spoiler Attack – Eagle View
Virtual Address
Physical Address
Physical Memory
JavaScript
malicious program
VA = PA
Perform Spoiler Attack
If
VA = PA?
PA revealed to user program

## Slide 9: Implementation Plan

## Slide 10: Implementation Plan
Access vHPCs
Linux
Timing
Record Latency
Obtain VA
Access ‘pagemap’
Obtain PA
Match with VA
Coorelation to vHPCs
PAPI Library
Run Algorithm
Algorithm Implementation
Using C++
Uses PAPI Library
Ubuntu

## Slide 11: Changes to Implementation Plan
  Linux
  Inline Assembly
  Written in C
  Run Algorithm
Access vHPCs
  Record Latency
  Data Collection
Timing
  Linux
  PAPI Library
  Run Algorithm
Access vHPCs
  Record Latency
  Coorelation to vHPCs
Timing
Algorithm Implementation
Using C++
Uses PAPI Library
Ubuntu
Algorithm Implementation
Using C
Ubuntu
Inline Assembly

## Slide 12: Revised Implementation Plan
Access vHPCs
Linux
Timing
Record Latency
Obtain VA
Access ‘pagemap’
Obtain PA
Match with VA
Inline Assembly
Written in C
Run Algorithm
Data Collection
Algorithm Implementation
Using C
Ubuntu
Inline Assembly
X

## Slide 13: Platform
Host OS: Microsoft Windows 10
VMware WorkStation Pro
Ubuntu
PageMapping
Spoiler Program
Inline Assembly
vHPC Enabled
rdtscp()
Host System:
Intel i7-7700 3.60GHz with 4 Physical and 8 Logical
16GB RAM
Hyper-V Enabled
Virtual System:
Intel i7-7700 3.60GHz with 2 Physical and 4 Logical
8GB RAM
Ubuntu 18.04 LTS 64-bit
Virtual Hardware Performance Counters Enabled

## Slide 14: Seek the Oracle …

## Slide 15: Implementation

## Slide 16: Pseudocode
Address Aliasing
for p from w to PAGE_COUNT do
for i from w to 0 do
data buffer[(p-i) × PAGE_SIZE]
end for
t1 = rdtscp()
data buffer[X × PAGE_SIZE]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
Timing Measurement of Speculative Load
rdtscp;
mov %eax, %esi;
mov (%rbx), %eax;
rdtscp;
mfence;
sub %esi, %eax;
HPC: Hardware Performance Counters, keep a track of low-level hardware-related events in the CPU, accessed via special purpose registers.
PAPI: Performance API
Read Time-Stamp Counter and Processor ID
Performs serializing operation on all preceding load/store instructions
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 17: Initialization
buffer[]=PAGE_COUNT; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from w to PAGE_COUNT do
for i from w to 0 do
data buffer[(p-i) × PAGE_SIZE]
end for
t1 = rdtscp()
data buffer[X × PAGE_SIZE]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
Window
=
64
Buffer
0
1000
....
4096 = 4k
4096 = 4k
4096 = 4k
4096 = 4k
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 18: Outer for
buffer[]=1000; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from w to PAGE_COUNT do
for i from w to 0 do
data buffer[(p-i) × PAGE_SIZE]
end for
t1 = rdtscp()
data buffer[X × PAGE_SIZE]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 19: Outer for
buffer[]=1000; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from 64 to 1000 do
for i from w to 0 do
data buffer[(p-i) × PAGE_SIZE]
end for
t1 = rdtscp()
data buffer[X × 4096]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
0
1000
....
Buffer
t1 = rdtscp()
data (load) buffer [X × PAGE_SIZE]
t2 = rdtscp()
measure [p] <- (t2 – t1)
64
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 20: Inner for
buffer[]=1000; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from w to PAGE_COUNT do
for i from w to 0 do
data buffer[(p-i) × PAGE_SIZE]
end for
t1 = rdtscp()
data buffer[X × PAGE_SIZE]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
for i from w to 0 do
data (store) buffer[(p-i) × PAGE_SIZE]
end for
0
....
Buffer
1000
WINDOW
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 21: Inner for
buffer[]=1000; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from w to PAGE_COUNT do
for i from 64 to 0 do
data buffer[(64-64) × 4096]
end for
t1 = rdtscp()
data buffer[X × PAGE_SIZE]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
for i from 64 to 0 do
data (store) buffer[(64-64) × 1000]
end for
0
....
Buffer
1000
WINDOW
4096 = 4k
64
0
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 22: Execution
buffer[]=PAGE_COUNT; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from 64 to 1000 do
for i from 64 to 0 do
data buffer[(p-i) × 4096]
end for
t1 = rdtscp()
data buffer[ X × 4096]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
p = 64
i = 64
data -> buffer[(64-64) × 4096] = 0
i = 63
data -> buffer[(64-63) × 4096] = 4096
.
.
i = 0
data -> buffer [(64-0) × 4096] = 262,144
t1 = rdtscp()
data buffer[ X × 4096]
t2 = rdtscp()
measure [p] <- t2-t1
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 23: Execution
buffer[]=PAGE_COUNT; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from 64 to 1000 do
for i from 64 to 0 do
data buffer[(p-i) × 4096]
end for
t1 = rdtscp()
data buffer[ X × 4096]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
p = 65
i = 64
data -> buffer[(65-64) × 4096] = 4096
i = 63
data -> buffer[(65-63) × 4096] = 8192
.
.
i = 0
data -> buffer [(65-0) × 4096] = 266,240
t1 = rdtscp()
data buffer[ X × 4096]
t2 = rdtscp()
measure [p] <- t2-t1
262,144
0
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 24: Execution
buffer[]=PAGE_COUNT; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from 64 to 1000 do
for i from 64 to 0 do
data buffer[(p-i) × 4096]
end for
t1 = rdtscp()
data buffer[ X × 4096]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
p = 1000
i = 64
data -> buffer[(1000-64) × 4096] = 3,833,856
i = 63
data -> buffer[(65-63) × 4096] = 8192
.
.
i = 0
data -> buffer [(1000-0) × 4096] = 4,096,000
t1 = rdtscp()
data buffer[ X × 4096]
t2 = rdtscp()
measure [p] <- t2-t1
4,091,904
3,829,760
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 25: Execution
buffer[]=PAGE_COUNT; PAGE_COUNT=1000; PAGE_SIZE=4096; windo(w)=64;
for p from 64 to 1000 do
for i from 64 to 0 do
data buffer[(p-i) × 4096]
end for
t1 = rdtscp()
data buffer[ X × 4096]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
. . . . . . .
Page 1000
Page 999
Page 998
Page 3
Page 2
Page 1
Page 0
Window
(Inner for)
Window
(Inner for)
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 26: Results

## Slide 27: Speculative Load Hazards
Loosenet Hit?
Finenet Hit?
Physical Address Match?
Partial Physical Addr Hit?
Redispatch Load
Proceed with Load
Block Load/
Forward Store
Yes
No
No
No
Yes
Yes
No
Yes
No
Dependency Resolution Check Logic
  Loosenet: Page offsets of load and store compared.
  Finenet: Checks upper virtual address bits, or the physical address tag.
  Physical Address Matching: Full physical address checked.
‘load’ checked against all preceding ‘store’ to ensure correctness
Notes: Page offset is identical between VA and PA, loosenet can be performed as soon as store is decoded. Dependency resolution may fail to resolve dependency.

## Slide 28: Code
for (int p = w; p <= PAGE_COUNT; p++){
for (int i = w; i >= 0; i--){
buffer[(p-i) * PAGE_SIZE] = DATA;
}
__asm__("CPUID\n\t"
"RDTSCP\n\t"
"mov %%edx, %0\n\t"
"mov %%eax, %1\n\t": "=r" (cycles_high), "=r" (cycles_low)::
"%rax", "%rbx", "%rcx", "%rdx");
DATA = buffer[X * PAGE_SIZE];
__asm__("RDTSCP\n\t"
"mov %%edx, %0\n\t"
"mov %%eax, %1\n\t"
"CPUID\n\t": "=r" (cycles_high1), "=r" (cycles_low1)::
"%rax", "%rbx", "%rcx", "%rdx");
measure[p] = cycles_low1-cycles_low;
printf("%d\n", measure[p]);
}
buffer[]=PAGE_COUNT;
PAGE_COUNT=1000;
PAGE_SIZE=4096;
windo(w)=64;
for p from w to PAGE_COUNT do
for i from w to 0 do
data buffer[(p-i) × PAGE_SIZE]
end for
t1 = rdtscp()
data buffer[X × PAGE_SIZE]
t2 = rdtscp()
measure [p] <- t2-t1
end for
return measure
Notes: Algorithm: executes a speculative load after multiple stores and make sure that 4K aliasing is caused during execution of the load. With w as the window size, algo iterates over a number of different memory pages and for each page performs stores to that page and all previous pages within a window. W=64. Making sure max # of entries are made in store buffer and hence maximum potential conflicts.

## Slide 29: Expected Results
From the paper, high latency appears once in every 256 page.

## Slide 30: Actual Results
Chart: 
From our experiment, high latency appears to fluctuate.

## Slide 31: Mitigation

## Slide 32: Software Mitigations
No software mitigation to completely erase this problem
Unable to enforce store fences in user’s code space
User can always leak the physical address information
JavaScript, remove access to accurate timers from browsers
But, removing timers removes the precision too and is impractical!

## Slide 33: Hardware Mitigations
Performance is impacted if speculative behavior is modified
Partial Address Comparison in Dependency Check Logic was for performance
Solution: Full Address Comparison but performance is impacted
Hardware patches are difficult to be deployed!

## Slide 34: Future Work

## Slide 35: Future Work
Utilize pagemap
Set of interfaces in kernel to examine page tables
4 main components
/proc/pid/pagemap
  Allows userspace process find out which physical frame each virtual page is mapped to
  64-bit value for each page

## Slide 36: Future Work
mmap() in Linux creates new mapping in virtual address space
Embed ‘spoiler.c’ into a new program with a mmap() wrapper
Proceed with same iteration pattern
Explicit creation of memory mapped pages
Record the latency and match with pagemap file

## Slide 37: Reference
Saad, Moghimi, Ahmad, Bruhns, Ida, Krebbel, Moritz, Berk, Eisenbarth, Thomas, and Berk, “SPOILER: Speculative Load Hazards Boost Rowhammer and Cache Attacks,” [astro-ph/0005112] A Determination of the Hubble Constant from Cepheid Distances and a Model of the Local Peculiar Velocity Field, 01-Mar-2019. [Online]. Available: https://arxiv.org/abs/1903.00446. [Accessed: 08-Mar-2019].
Y. Kim, R. Daly, J. Kim, C. Fallin, J. H. Lee, D. Lee, C. Wilkerson, K. Lai, O. Mutlu, Carnegie Mellon University, and Intel Labs, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” IEEE Xplore Digital Library, 14-Jul-2014. [Online]. Available: https://ieeexplore.ieee.org/document/6853210. [Accessed: 04-Apr-2019].
L. Tung, “All Intel chips open to new Spoiler non-Spectre attack: Don't expect a quick fix,” ZDNet, 05-Mar-2019. [Online]. Available: https://www.zdnet.com/article/all-intel-chips-open-to-new-spoiler-non-spectre-attack-dont-expect-a-quick-fix/. [Accessed: 28-Mar-2019].
“SPOILER,” AMD . [Online]. Available: https://www.amd.com/en/support/kb/faq/pa-240. [Accessed: 28-Mar-2019].
“Distribution of AMD and Intel x86 computer processors worldwide, from 2012 to 2018, by quarter,” statista. [Online]. Available: https://www.statista.com/statistics/735904/worldwide-x86-intel-amd-market-share/. [Accessed: 05-Apr-2019].

## Slide 38: Questions?